## Slide 1
Outline
Brief introduction to testbed topology
Some studies about BGP
Minimum requirement for testbed

## Slide 2
Testbed topology: ideal
AS ID: 65535
AS ID: 65100
AS ID: 65200
AS ID: 65501
AS ID: 65502
AS ID: 65503
AS ID: 65504

## Slide 3
Testbed topology: reconfigured

## Slide 4
Testbed topology: reconfigured

## Slide 5
BGP study: switch processing time of BGP UPDATE
Time to send BGP UPDATE messages to neighbors after detecting link failures: not measured.
Time to process BGP UPDATE messages received from neighbors: about 1ms.

## Slide 6
Measurement of switch processing time of BGP UPDATE
t1
t2
t2 – t1 is an estimation of switch processing time of BGP UPDATE messages.

## Slide 7
t1
t1’
t1’ ≈ t1
Measurement of switch processing time of BGP UPDATE

## Slide 8
t1’
t2
t2 – t1’ ≈ t2 – t1 ≈ an estimation of switch processing time of BGP UPDATE messages.
Measurement of switch processing time of BGP UPDATE

## Slide 9
BGP UPDATE messages from L3 to S1 and S2:
BGP UPDATE messages from L3 to switch S1 and from S2 to L1:
t1 = 0.000000s, t1’ = 0.000043s, t1’ ≈ t1
t1’ = 0.000000s, t2 = 0.000938s, t2 – t1’ ≈ t2 – t1 ≈ 0.938 ms
It will take a switch about 1ms to process BGP messages from last hop and generate BGP message to next hop.
Measurement of switch processing time of BGP UPDATE

## Slide 10
BGP UPDATE message

## Slide 11
Some calculations about PFC deadlock
It may take BGP only a few milliseconds to delete all the routes to the failure switch.
Time to create a k-hop PFC deadlock = tPFC*k/B.
let tPFC = 25KB, k = 4, B = 40Gbps, the time would be
25KB*4/40Gbps = 20us << 1ms

## Slide 12
BGP study: route aggregation
169.254.0.0/16 -> Eth29
172.16.0.0/16 -> Eth29

## Slide 13
Minimum testbed requirement

## Slide 14
H2: 10.1.1.1
H1: 10.0.0.1
10.0.0.0/16 -> L1
10.1.1.0/24 -> T4
Default -> S1, S2
10.1.0.0/16 -> L3, L4
L3
L4
T4
L1
T1
S 1
S 2
Backup: PFC deadlock case