## Slide 1
Outline
Experiment results of PFC deadlock cases
Some analysis about PFC deadlock

## Slide 2
Testbed information
Some testbed parameters:
  Default TTL of RDMA packets: 16;
  Switch forwarding-mode: store-and-forward;
  Link capacity: 40Gbps;
  Switch buffer size: 12MB;
  Configured maximum frame size: 1024 bytes;

## Slide 3
H2: 172.16.4.5
H1: 172.16.3.6
172.16.4.0/31 -> T4
L3
L4
T4
L1
T1
S1
S2
PFC deadlock experiment-A
T3
172.16.4.5/32 -> L4
30
2
30
40Gbps
1

## Slide 4
H2: 172.16.4.5
H1: 172.16.3.6
L3
L4
T4
L1
T1
S1
S2
PFC deadlock experiment-B
T3
172.16.4.5/32 -> L4
30
2
30
40Gbps
1
172.16.4.5/32 -> S1
172.16.4.5/32 -> L3

## Slide 5
More experiment results
Message size(KB) | 2.2 | 2.5 | 5 | 10 | 60
Sending rate(Gbps) | 10 | 11.5 | 22 | 38 | 40
PFC deadlock | No | Yes | Yes | Yes | Yes
Experiment results of 2-hop loop:
Message size(KB) | 3.5 | 4100 | 4.5 | 10 | 60
Sending rate(Gbps) | 15 | 20 | 24.5 | 38 | 40
PFC deadlock | No | No | Yes | Yes | Yes
Experiment results of 4-hop loop:

## Slide 6
Takeaways of the two experiments
According to our analysis last week, TTL*one-hop-delay ≈ 16 * 0.2us = 8us should be a tight bound for PFC deadlock.
  At rate 40Gbps, Only about 40KB packets can be injected into the loop within 8us, which is far smaller than the PFC threshold (measured threshold is about 2MB).

## Slide 7
Takeaways of the two experiments
According to our analysis last week, TTL*one-hop-delay ≈ 16 * 0.2us = 8us should be a tight bound for PFC deadlock.
  At rate 40Gbps, Only about 40KB packets can be injected into the loop within 8us, which is far smaller than the PFC threshold (measured threshold is about 2MB).
Two factors we need to consider when analyzing PFC deadlock:
  Queuing delay in the routing loop.
  PFC threshold is dynamic.

## Slide 8
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
*Let the time to send one 1KB pkt at rate 40Gbps to next hop as one time unit (~0.2us).
Impact of queuing delay on PFC deadlock
Time unit 0:
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
queueing delay of the 1st pkt

## Slide 9
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
*Let the time to send one 1KB pkt at rate 40Gbps to next hop as one time unit (~0.2us).
Time unit 1:
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
queueing delay of the 1st pkt
Impact of queuing delay on PFC deadlock

## Slide 10
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
*Let the time to send one 1KB pkt at rate 40Gbps to next hop as one time unit (~0.2us).
Time unit 2:
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
#2 | 2 | 1 | 13
queueing delay of the 1st pkt
Impact of queuing delay on PFC deadlock

## Slide 11
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
*Let the time to send one 1KB pkt at rate 40Gbps to next hop as one time unit (~0.2us).
Time unit 191:
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
#2 | 2 | 1 | 13
#3 | 5 | 4 | 11
#4 | 11 | 10 | 9
#5 | 23 | 22 | 7
#6 | 47 | 46 | 5
#7 | 95 | 94 | 3
#8 | 191 | 190 | 1
queueing delay of the 1st pkt
Impact of queuing delay on PFC deadlock
The first packet will expire at time unit 15 without queuing delay.

## Slide 12
Analysis of the steady-state
r
B - rd
B
r | Inject rate of new packets.
B | Link bandwidth.
rd | Drain rate of packets caused by TTL expiration.
 | TTL value.
n | Hop number of routing loop.
r | Inject rate of new packets.
B | Link bandwidth.
rd | Drain rate of packets caused by TTL expiration.
 | TTL value.
n | Hop number of routing loop.
Two observations:
  input rate = output rate;
  The sum of TTLs of all pkts should be the fixed in a long-term view.

## Slide 13
Analysis of the steady-state
r
B - rd
B
Case 1: packets are dropped at the congestion hop (hop 1).
Case 2: packets are dropped at some uncongested hop (hop k).
consuming rate of TTL
generating rate of TTL
consuming rate of TTL
generating rate of TTL

## Slide 14
Analysis of the steady-state
r
B - rd
B
Case 1: packets are dropped at the congestion hop (hop 1).
Case 2: packets are dropped at some uncongested hop (hop k).

## Slide 15
There is a difference between analysis and experiment results
Message size(KB) | 2.2 | 2.5 | 5 | 10 | 60
Sending rate(Gbps) | 10 | 11.5 | 22 | 38 | 40
PFC deadlock | No | Yes | Yes | Yes | Yes
Experiment results of 2-hop loop:
Message size(KB) | 3.5 | 4.1 | 4.5 | 10 | 60
Sending rate(Gbps) | 15 | 20 | 24.5 | 38 | 40
PFC deadlock | No | No | Yes | Yes | Yes
Experiment results of 4-hop loop:
= 5Gbps
= 10Gbps
Possible reasons:
  The arrival intervals between pkts is not the same (microburst).
  PFC pause messages can reduce the queuing delay.

## Slide 16
H2: 172.16.4.5
H1: 172.16.3.6
172.16.4.0/31 -> T4
L3
L4
T4
L1
T1
S1
S2
PFC threshold is dynamic
T3
172.16.4.5/32 -> L4
30
2
30
40Gbps
1

## Slide 17
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
3.5MB
2MB
2MB
Switch | PFC threshold + headroom
T3 | 2 MB
T4 | 2 MB
L4 | 3.5 MB/2 = ~ 1.75 MB
PFC threshold is dynamic

## Slide 18
H3: 172.16.4.5
H2: 172.16.3.6
172.16.3.6/32 -> S1
L3
L4
T4
L1
T1
S1
S2
T3
172.16.4.5/32 -> L4
30
2
30
40Gbps
1
H1: 172.16.1.2
29
PFC threshold is dynamic

## Slide 19
L4
T4
L4-1-rx
L4-2-rx
T4-30-rx
T4-30-tx
T3
T3-30-tx
L4-2-tx
2.8MB
2MB
2MB
Switch | PFC threshold + headroom
T3 | 2 MB
T4 | 2 MB
L4 | 2.8MB/2 = 1.4 MB
L4-29-rx
some buffer is occupied.
2.1MB
PFC threshold is dynamic