## Slide 1
Outline
Routing induced deadlock and solution
  The routing configuration is not deadlock-free.
  Network reconfiguration and network failure.
Resource induced Deadlock and solution
  Buffer circular dependence
  Priority blocking (improperly called deadlocks)

## Slide 2
Outline
Routing induced deadlock and solution
  The routing configuration is not deadlock-free.
  Network reconfiguration and network failure.
Resource induced Deadlock and solution
  Buffer circular dependence
  Priority blocking (improperly called deadlocks)

## Slide 3
A selective list of related papers
Deadlock-free routing algorithms:
  Deadlock-Free Message Routing in Multiprocessor Interconnection Networks, TOC, 1987
  Layered shortest path (LASH) routing in irregular system area networks, IPDPS 2002
  Practical DCB for Improved Data Center Networks, INFOCOM 2014
Deadlock detection and recovery algorithms:
  4. An efficient, fully adaptive deadlock recovery scheme: DISHA, Computer Architecture, 1995
  5. Generalized Theory for Deadlock-Free Adaptive Wormhole Routing and its Application to Disha Concurrent, IPPS, 1996

## Slide 4
Sufficient and necessary condition for deadlock-free routing
S2
S1
S3
S4
A lossless network N and a routing configuration R.
S2
S1
S3
S4
Queue dependency graph.
Routing path
Theorem 1 (proved in [1]): A routing configuration R for a network N is deadlock free iff there are no cycles in the queue dependency graph.
Note that theorem 1 only considers the routing aspect. In fact, a deadlock-prone routing configuration will not necessarily lead to a deadlock.

## Slide 5
Reconfiguration or failure induced deadlocks
During the network reconfiguration process or when a network failure happens:
  The network can be a mix of old and new routing rules.
  Cyclic queue dependency may exist even if the old and new routing configurations independently are deadlock-free.
S2
S1
S3
S4
New paths
Old paths

## Slide 6
Solution: routing induced deadlocks
Deadlock avoidance solution:
  a) Find a set of deadlock-free paths as the legal routing paths.
  *drawback: network bandwidth can be wasted as many routing paths are not used.
  b) Divide the routing paths into several virtual channels (each channel is associated with a priority) and ensure that the paths in each channel is deadlock-free.
  *drawback: the number of needed priorities can be much larger than 8.

## Slide 7
Solution: routing induced deadlocks
Deadlock detection and recovery solution:
  a) Set a timeout value in each switch to detect the deadlock.
  *drawback: 1) a too small timeout value will lead to many false detections while a too large value will make the reaction too slow. 2) The timeout based detection requires the switch to monitor the blocked time of every output queue which is not available for commodity switches.
  b) Once a deadlock is detected, the switch drops some of the blocked packets. An alternative way is to reserve some dedicated buffer for deadlock-recovery.
  *drawback: A distributed solution may drop too many packets while a centralized solution or a coordination based solution is too slow.

## Slide 8
Solution: reconfiguration or failure induced deadlocks
Static reconfiguration (not work for failure case)
  Pause the network
  Update the routing function
  Resume flow transmissions relying on upper layer protocols
Dynamic reconfiguration
  Design a well-planed routing update plan (not work for failure case)
  Apply deadlock detection and recovery solutions

## Slide 9
Routing induced Deadlocks in RDMA data centers
Previous deadlock avoidance solution is useless:
  For Clos network, we already proved that the set of all shortest paths is deadlock-free. So we don’t need any deadlock-free routing algorithms.
Previous deadlock detection and recovery solution is not desired:
  Timeout value seems to be a magic number;
  Timeout based detection is not directly supported by commodity switch.
Takeaway: we need a new deadlock detection and recovery mechanism for Clos network to handle reconfiguration or failure induced deadlocks.

## Slide 10
Routing induced Deadlocks in RDMA data centers
Goals of deadlock detection and recovery:
  Fast reaction: a distributed solution without coordination between switches;
  Directly supported by commodity switches;
  Minimize the number of false detections;
Preliminary idea: TTL based detection
  Observation: In a regular Clos network, for any given switch, the TTL value of all incoming or outgoing pkts should be some fixed values when all flows are routed over shortest paths;
  Solution:
    Each switch set some filters to detect the pkts with unexpected TTL values.
    Once detected, the switch periodically reads the number of PFC pause frames received or sent at related queues and estimates an increase rate of PFC pause frames.
    If the increase rate exceeds a threshold, the switch change the related port(s) to be lossy.

## Slide 11
Outline
Routing induced deadlock and solution
  The routing configuration is not deadlock-free.
  Network reconfiguration and network failure.
Resource induced Deadlock and solution
  Buffer circular dependence
  Priority blocking (improperly called deadlocks)

## Slide 12
Deadlock caused by Buffer circular dependence
A
B
Packets of flow 1 and flow 2 occupy all the buffer of switch A;
Packets of flow 3 and flow 4 occupy all the buffer of switch B;
Solution: no input port is allowed to consume more than 1/N of the shared memory.
*Unlikely to happen in production data centers as long as ECN is enabled.
Flow 1
Flow 3
Flow 2
Flow 4

## Slide 13
Priority blocking problem
C
D
Flow 1
Flow 3 blocked
B
Flow 2
Priority order of flows: P3 > P1 > P2
Flow 3 arrives later and is blocked as all the buffer is already occupied by flow 2. Note that Flow 3 has the highest priority.
Solution: reserve dedicated buffer for each priority.
*Unlikely to happen in production data centers as long as ECN is enabled.