## Slide 1
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause
Analyze deadlock Case with Statistical Model
Outline

## Slide 2
Outline
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause
Analyze deadlock Case with Statistical Model

## Slide 3
Statistical Model - Terms
Time unit ∆t: the time for a device to send one packet to next-hop device.
  Assumption: We assume a PAUSE frame can take effect immediately and lasts for ∆t.
Pause event pause(j, i, ∆tk): pause(j, i, ∆tk) =1 means switch j will pause switch i at time unit ∆tk.
Pause probability P(pause(j, i, ∆tk)): the probability for event pause(j, i, ∆tk) to occur.
pause
j
tx
rx
i
tx
rx
rc
r1 (> rc)
flow 1
B

## Slide 4
pause
Pause Event
T
Statistical Model – Computation of P(pause(j, i, ∆tk))
2
tx
rx
1
tx
rx
Case 1: Capacity Bounded Pause
rc
r1 (> rc)
flow 1
rc = B  n = (B- rc )/ rc
  E.g., When rc = B/4, n = 3.
P( pause(2, 1, ∆tk)=1 ) = n/(n+1) = 1-rc/B
B
P
…
P
T
P
P
…
P
T
Non-Pause Event
T
P
P
…
……
n

## Slide 5
Case 2: Head-of-Line Blocking Pause
Statistical Model – Computation of P(pause(j, i, ∆tk))
Question: P( pause(1, 4, ∆tk)=1 ) = ? when r2 is set to different values.
4
flow 2
r2
rc
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
P( pause(2, 1, ∆tk)=1 )=1-rc/B when 2*rc <= B
?
tx
rx
rx-2
tx

## Slide 6
Case 2: Head-of-Line Blocking Pause
Condition 1: r2 < rc  P( pause(1, 4, ∆tk)=1 ) = 0
4
flow 2
r2
r2
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
?
tx
tx
rx
rx-2
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 7
Simulation Results when setting rc = B/2=20Gbps, r2 =B/4=10Gbps:
At switch 1, queue length of flow 2 is half of flow 1’s, which complies with their drain rates at switch 1.
Almost no packets are queued at switch 4.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
1/2
1
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 8
Case 2: Head-of-Line Blocking Pause
Condition 2: r2 = rc  P( pause(1, 4, ∆tk)=1 ) = 1-rc/B
4
flow 2
r2
rc
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
P( pause(2, 1, ∆tk)=1 )=1-rc/B
?
tx
tx
rx
rx-2
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 9
Simulation Results when setting rc = B/2=20Gbps, r2 =B/2=20Gbps:
At switch 1, queue length of flow 2 is the same as flow 1’s, which complies with their drain rates at switch 1.
Some packets are queued at switch 4. Switch 4 is paused by switch 1 intermittently.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 10
Case 2: Head-of-Line Blocking Pause
Condition 3: r2 > rc  P( pause(1, 4, ∆tk)=1 ) = 1-rc/B
4
flow 2
r2
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
P( pause(2, 1, ∆tk)=1 )=1-rc/B
?
tx
tx
rx
rx-2
rc
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 11
Simulation Results when setting rc = B/2=20Gbps, r2 =B=40Gbps:
At switch 1, queue length of flow 2 is the same as flow 1’s, which complies with their drain rates at switch 1.
Packets are queued at switch 4 and exceed PFC threshold. Switch 4 is paused by switch 1 intermittently.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 12
Outline
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause
Analyze deadlock Case with Statistical Model

## Slide 13
Analyze Deadlock Case with Statistical Model
A
rx
tx
B
C
tx
rx
flow 1
flow 2
flow 3
r1 = B
r2 = B
r3 = B
tx
rx
Case 1:
Injection rates of three flows are B.

## Slide 14
Analyze Deadlock Case with Statistical Model
A
rx
tx
B
C
tx
rx
flow 2
flow 3
tx
rx
Case 1:
flow 1
r1 = B
Tx queues of switches A, B and C are equivalent. We consider the pause event from B to C.
As we have r3 >= B/2 at the link C-B, P( pause(B, C, ∆tk)=1 ) = 1-rc/B = 0.5
P = 0.5
rc = B/2
r2 = B
r3 = B
r3 >= B/2

## Slide 15
Analyze Deadlock Case with Statistical Model
A
rx
tx
B
C
tx
rx
flow 2
flow 3
tx
rx
Case 1:
flow 1
r1 = B
Probability of deadlock event = 0.5^3 = 0.125 >0, deadlock can occur.
NS-3 simulation shows that deadlock will occur in this case.
P = 0.5
r2 = B
r3 = B
P = 0.5
P = 0.5

## Slide 16
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 2:
Rate limiting = B/2
r1 = B
r2 = B
Injection rates of both flows are B.

## Slide 17
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 1
Case 2:
r1 = B
Rate limiting = B/2
P = 0.5
P = 0.5
r1 = B/2
Consider flow 1 at first.

## Slide 18
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 2:
r1 = B
r2 = B
Rate limiting = B/2
P = 0.5
P = 0.5
P = 0.5
r2 = B/2
P = 0.5
P = 0
r1 = B/2
Probability of deadlock event = 0.5^3*0 = 0, deadlock can occur.
NS-3 simulation shows that deadlock will not occur in this case.

## Slide 19
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 3:
Rate limiting = B/2
r1 = B
r2 = B
flow 3
r3 = B
Injection rates of three flows are B.

## Slide 20
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 1
Case 3:
r1 = B
Rate limiting = B/2
P = 0.5
P = 0.5
r1 = B/2
flow 3
r3 = B
Consider flow 1 and flow 3. Rate limiting at tx-2 queue of S4 will no longer take effect.
P = 0.5
r1 = B/2
r3 = B/2

## Slide 21
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 3:
r1 = B
r2 = B
Rate limiting = B/2
P = 0.5
P = 0.5
r2 = B/2
P = 0.5
P = 0.5
r1 = B/2
Probability of deadlock event = 0.5^4 > 0, deadlock can occur.
NS-3 simulation shows that deadlock will occur in this case.
flow 3
r3 = B
P = 0.5

## Slide 22
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 4:
Rate limiting = B/2
r1 = B
r2 = B
flow 3
r3 = B
Injection rates of four flows are B.
r4 = B
flow 4

## Slide 23
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Case 4:
r1 = B
r2 = B
Rate limiting = B/2
P = 2/3
r2 = B/3
P = 2/3
P = 2/3
r1 = B/3
Probability of deadlock event = (2/3)^4 >0, deadlock can occur.
NS-3 simulation shows that deadlock will occur in this case.
r3 = B
r4 = B
flow 4
flow 3
P = 2/3
P = 2/3
P = 2/3

## Slide 24
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 1
Case 4:
r1 = B
Rate limiting = B/2
P = 0.5
P = 0.5
r1 = B/2
Consider flow 1 at first.

## Slide 25
Analyze Deadlock Case with Statistical Model
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 1
Case 4:
r1 = B
Rate limiting = B/2
P = 2/3
r1 = B/3
Consider flow 3 and flow 4.
P = 2/3
flow 3
r3 = B
r4 = B
flow 4
P = 2/3