## Slide 1
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause (Modified)
    Deadlock Case Analysis (Modified)
Outline

## Slide 2
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause (Modified)
    Deadlock Case Analysis (Modified)
Outline

## Slide 3
Statistical Model - Terms
Time unit ∆t: the time for a device to send one packet to next-hop device.
  Assumption: We assume a PAUSE frame can take effect immediately and lasts for ∆t.
Pause event pause(j, i, ∆tk): pause(j, i, ∆tk) =1 means switch j will pause switch i at time unit ∆tk.
Pause probability P(pause(j, i, ∆tk)): the probability for event pause(j, i, ∆tk) to occur.
pause
j
tx
rx
i
tx
rx
rc
r1 (> rc)
flow 1
B

## Slide 4
pause
Pause Event
T
Statistical Model – Computation of P(pause(j, i, ∆tk))
2
tx
rx
1
tx
rx
Case 1: Capacity Bounded Pause
rc
r1 (> rc)
flow 1
rc = B  n = (B- rc )/ rc
  E.g., When rc = B/4, n = 3.
P( pause(2, 1, ∆tk)=1 ) = n/(n+1) = 1-rc/B
B
P
…
P
T
P
P
…
P
T
Non-Pause Event
T
P
P
…
……
n

## Slide 5
Case 2: Head-of-Line Blocking Pause
Statistical Model – Computation of P(pause(j, i, ∆tk))
Question: P( pause(1, 4, ∆tk)=1 ) = ? when r2 is set to different values.
4
flow 2
r2
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
P( pause(2, 1, ∆tk)=1 ) = 1-(r2’+rc)/B
?
tx
rx
rx-2
tx
r2’

## Slide 6
Case 2: Head-of-Line Blocking Pause
Condition 1: r2 < rc  P( pause(1, 4, ∆tk)=1 ) = 0
4
flow 2
r2
r2
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
?
tx
tx
rx
rx-2
Statistical Model – Computation of P(pause(j, i, ∆tk))
P( pause(2, 1, ∆tk)=1 ) = 1-(r2+rc)/B >0

## Slide 7
Simulation Results when setting rc = B/2=20Gbps, r2 =B/4=10Gbps:
At switch 1, queue length of flow 2 is half of flow 1’s, which complies with their drain rates at switch 1.
Almost no packets are queued at switch 4.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
1/2
1
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 8
Case 2: Head-of-Line Blocking Pause
Condition 2: r2 = rc  P( pause(1, 4, ∆tk)=1 ) = 1-rc/B
4
flow 2
r2
rc
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
?
tx
tx
rx
rx-2
Statistical Model – Computation of P(pause(j, i, ∆tk))
P( pause(2, 1, ∆tk)=1 ) = 1-2rc/B >= 0
When rc=B/2, P( pause(2, 1, ∆tk)=1 ) =0

## Slide 9
Simulation Results when setting rc = B/2=20Gbps, r2 =B/2=20Gbps:
At switch 1, queue length of flow 2 is the same as flow 1’s, which complies with their drain rates at switch 1.
Some packets are queued at switch 4. Switch 4 is paused by switch 1 intermittently.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 10
Simulation Results when setting rc = B/2=20Gbps, r2 =B/2=20Gbps:
Statistical Model – Computation of P(pause(j, i, ∆tk))
Instant drain rate of flow 1 and flow 2 at switch 1
At switch 1, both flows get drained at the rate of ~20Gbps which indicates that P( pause(2, 1, ∆tk)=1 ) =0.
Question: Why does the queue length of switch 4‘s tx queue is larger than 0? (answered in next slide)

## Slide 11
Case 2: Head-of-Line Blocking Pause
At the very beginning, It will take some time for green packets to gradually achieve rate rc at switch 1. During this period, we have r2 < rc and a small part of green packets get queued at switch 4.
This part of packets will never be drained under the condition when r2 = rc at the sender, and it will cause P( pause(1, 4, ∆tk)=1 ) = 1-rc/B.
4
flow 2
r2
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
?
tx
tx
rx
rx-2
Statistical Model – Computation of P(pause(j, i, ∆tk))
r2=0

## Slide 12
Case 2: Head-of-Line Blocking Pause
Condition 3: r2 > rc  P( pause(1, 4, ∆tk)=1 ) = 1-rc/B
4
flow 2
r2
pause
pause
2
tx
rx
1
tx
rx
rc
r1 (> rc)
flow 1
B
3
P( pause(2, 1, ∆tk)=1 )=1-rc/B
?
tx
tx
rx
rx-2
rc
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 13
Simulation Results when setting rc = B/2=20Gbps, r2 =B=40Gbps:
At switch 1, queue length of flow 2 is the same as flow 1’s, which complies with their drain rates at switch 1.
Packets are queued at switch 4 and exceed PFC threshold. Switch 4 is paused by switch 1 intermittently.
Instant queue length of tx queue of switch 1
Instant queue length of tx queue of switch 4
Statistical Model – Computation of P(pause(j, i, ∆tk))

## Slide 14
Statistical Model
  Terms
  Probability of Pause Event:
    Capacity Bounded Pause
    Head-Of-Line (HOL) Blocking Pause (Modified)
    Deadlock Case Analysis (Modified)
Outline

## Slide 15
Analyze Deadlock Case with Statistical Model
flow 3
Case 1:
Injection rates of three flows are B. For the ease of analysis, we start flow 1 and flow 2 at first, and then start flow 3.
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
flow 1
r1 = B
r2 = B
r3 = B

## Slide 16
Analyze Deadlock Case with Statistical Model
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
Case 1:
flow 1
r1 = B
Packets will build up at the tx queues of switch A and switch B.
Let D be the PFC threshold (in packets). A pause frame will be generated when the queue occupancy related to one rx queue is D+1.
r2 = B
rc = B/2
 | Queue length of switch 1 | Queue length of switch 2 | Queue length of switch 3
Flow 1 | D | 0 | D
Flow 2 | D | 0 | 0
Flow 3 | 0 | 0 | 0
rc = B/2

## Slide 17
Analyze Deadlock Case with Statistical Model
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
Case 1:
flow 1
r1 = B
As queue occupancy is proportional to flow rate, the queue length of flow 3 at switch 2 and switch 3 will converge into D to achieve B/2 rate.
r2 = B
rc = B/2
 | Queue length of switch 1 | Queue length of switch 2 | Queue length of switch 3
Flow 1 | D | 0 | D
Flow 2 | D | D | 0
Flow 3 | 0 | D | D
flow 3
r3 = B
r3 >= B/2
rc = B/2

## Slide 18
Analyze Deadlock Case with Statistical Model
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
Case 1:
flow 1
r1 = B
We consider the color of first packet at three tx queues.
At time 0, it is possible that the first packet at 3-tx is red, the first packet at 1-tx is green, and the first packet at 2-tx is purple.
r2 = B
rc = B/2
 | Queue length of switch 1 | Queue length of switch 2 | Queue length of switch 3
Flow 1 | D | 0 | D
Flow 2 | D | D | 0
Flow 3 | 0 | D | D
flow 3
r3 = B
r3 >= B/2
rc = B/2
Start of time 0:

## Slide 19
Analyze Deadlock Case with Statistical Model
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
Case 1:
flow 1
r1 = B
At time 0, there is a chance that the first packet at each tx queue to be injected into the tail of the next-hop switch’s tx queue.
If not, the state of the network goes back to the initial state and start a new round.
r2 = B
rc = B/2
 | Queue length of switch 1 | Queue length of switch 2 | Queue length of switch 3
Flow 1 | D+1 | 0 | D-1
Flow 2 | D-1 | D+1 | 0
Flow 3 | 0 | D-1 | D+1
flow 3
r3 = B
r3 >= B/2
rc = B/2
End of time 0:

## Slide 20
Analyze Deadlock Case with Statistical Model
1
rx
tx
3
2
tx
rx
flow 2
tx
rx
Case 1:
flow 1
r1 = B
A deadlock occurs due to the cyclic pause.
r2 = B
rc = B/2
 | Queue length of switch 1 | Queue length of switch 2 | Queue length of switch 3
Flow 1 | D+1 | 0 | D-1
Flow 2 | D-1 | D+1 | 0
Flow 3 | 0 | D-1 | D+1
flow 3
r3 = B
r3 >= B/2
rc = B/2
Start of time 1:
Pause
Pause
Pause