## Slide 1
flow 3
Flow Convergence Time: Let t0 be the time we start all flows. Let t1 be the time that queue occupancy of three flows is around PFC threshold in related tx queues for the first time. We define t1 - t0 as the flow convergence time.
2
rx
tx
1
3
tx
rx
flow 2
tx
rx
flow 1
r1 = B
r2 = B
r3 = B
Study of Flow Convergence Time

## Slide 2
Flow Convergence Time - Exp1
PFC threshold= 20KB
PFC threshold= 40KB
Setting: link delay =0ms, link capacity = 8Gbps (1us to transmit a packet), start all three flows at time 0ms.
Observation: Flow convergence time is lineal to PFC threshold (e.g., ~0.08ms when PFC = 20KB, ~0.16ms when PFC = 40KB)
Instant queue length of tx queue of switch 1:
PFC threshold= 80KB

## Slide 3
Flow Convergence Time – Exp2
Link capacity= 10Gbps
Link capacity= 20Gbps
Setting: link delay =0ms, PFC threshold= 40KB (1us to transmit a packet), start all three flows at time 0ms.
Observation: Flow convergence time is lineal and inversely proportional to link capacity (e.g., ~0.13ms when link capacity = 10Gbps, ~0.065ms when link capacity = 20Gbps)
Instant queue length of tx queue of switch 1:
Link capacity= 40Gbps

## Slide 4
Link delay =0.001ms
Setting: PFC threshold= 40KB, link capacity = 8Gbps (1us to transmit a packet), start all three flows at time 0ms.
Observation: Flows do not converge when link delay is very large (e.g., 0.1ms)
Link delay =0.01ms
Link delay =0.1ms
Instant queue length of tx queue of switch 1:
Flow Convergence Time – Exp3