## Slide 1: Algorithm Input/Output
Input
  Topology: a graph of switches and links
  Lossless routes: the set of all routing paths that must be lossless
Output
  The Tag-based ACL rules and buffer configuration, s.t.,
    There is never cyclic buffer dependency (deadlock free)
    Never drop packets that follow lossless routes
Assumption
  There is a tagging system that tags the packet along the path.
Our design goal: minimize the # of lossless priorities and # of ACL rules

## Slide 2: Tagging System
Requirements
  Tags are changed monotonically along any packet’s path
  On each switch, packets are classified into different priority classes purely based on the tags
We have good heuristics for Clos and BCube
For general graphs, TTL is always a feasible solution
  However, it may not be optimal in terms of # of tags used – affecting the # of ACL rules

## Slide 3: Notations
Ai represents a unique ingress port: switch A’s ith ingress port
(Ai, x) is a port-tag pair: the case where Ai gets a packet with tag=x
V is the set of all port-tag pairs that appear in input lossless routes
(Ai, x)  (Bj, y) is a hop. It is essentially a buffer dependency.
  There exists a hop iff switch A and B are connected, AND switch A may change the tag from x to y before sending to B
E is the set of all hops whose two ends are both in V
G=(V, E) is the lossless graph.
Input
Topology
Lossless routes

## Slide 4: Algorithm Sketch
Step 1 (Alg. 1): divide G into induced subgraphs Si
  Input: topology, lossless routes
  Output: subgraphs Si , s.t.,
    V = V(S1) U V(S2) U … U V(Sn), V(Si)ꓵ V(Sj) = Ф, ejk E(Si) iff vj, vk V(Si) and ejk E
    The port-dependency graph of Si does NOT have a cycle
    There is no switch port that has both inter-Si edge and intra-Si edge (switch QoS limitation)
    There is no lossless route going from Si to Sj if i < j (monotonically non-increasing)
Step 2 (Alg. 2): generate ACL rules and buffer configurations
  Input: subgraphs Si
  Output: ACL and buffer configurations, s.t.,
    If a packet is at a port-tag pair in Si, it will be mapped to Si’s lossless class
    Once a packet has a hop not in Si, it will be immediately mapped to Sj (j<i) or lossy class
Ai | Switch A’s ith ingress port
(Ai, x) | Port-tag pair
(,)->(,) | A hop
V | All port-tag pairs in lossless routes
E | All lossless hops
G | G(V, E) Lossless graph
Input
Topology
Lossless routes
Subgraphs whose vertexes are a subset of V, edges exist iff they are present in E

## Slide 5: Alg. 1
For general graph, at least we have a greedy algorithm
  var output=Set(); var S=Set(); output.add(S);
  for (t=initial_tag; t>=0;)
  var left_over = False;
  4. for each port-tag pair v in the form of (Ai, t) in V
  5. S’  S U {v}
  6. if PDG(S’) is acyclic and does not have an edge same as inter-S, S S’, V  V \ {v};
  7. otherwise, left_over = True;
  8. if left_over, S=Set(), output.add(S);
  9. otherwise, t--;
  The Set output is how we divide G.
  This may not be optimal. Worst case: |output| = the diameter of G
Input
Topology
Lossless routes
Ai | Switch A’s ith ingress port
(Ai, x) | Port-tag pair
(,)->(,) | A hop
V | All port-tag pairs in lossless routes
E | All lossless hops
G | G(V, E) Lossless graph
PDG(): port dependency graph

## Slide 6: Side Note: Strawman
The strawman solution (map each TTL to a separate class) is also an algorithm for Step 1, as follows
Divide G into d subgraphs Si, s.t. Si ={(Aj, i) | Ɐ Aj}
We can check:
  V = V(S1) U V(S2) U … U V(Sn), V(Si)ꓵ V(Sj) = Ф, ejk E(Si) iff vj, vk V(Si) and ejk E
  Si does NOT have a cycle
  There is no switch port that has both inter-Si edge and intra-Si edge
  There is no lossless route going from Si to Sj if i < j (monotonically non-increasing)
It is far from optimal in terms of # of priorities
Input
Topology
Lossless routes
Ai | Switch A’s ith ingress port
(Ai, x) | Port-tag pair
(,)->(,) | A hop
V | All port-tag pairs in lossless routes
E | All lossless hops
G | G(V, E) Lossless graph

## Slide 7: Alg. 2 (Generate Switch Configs)
Assign a lossless class i for each Si
  Requires |Si| lossless classes
Ingress ACL rules: classify packets based on tags
  For each Si, for each (Aj, k) in Si, install a rule on switch A, port j, put packets with tag k into class i.
  All other packets are put into lossy class by default
  # of ACL rules required = # of port-pair tags
PFC-priority mapping for inter-Si hop:
  e.g., (Am, x)  (Bn, y), where (Am, x) Si , (Bn, y) Sj , i>j
  On switch A, egress port towards B, when receive PAUSE of priority j, pause priority i
Ai | Switch A’s ith ingress port
(Ai, x) | Port-tag pair
(,)->(,) | A hop
V | All port-tag pairs in lossless routes
E | All lossless hops
G | G(V, E) Lossless graph

## Slide 8: Example
A 3-node topology with TTL as the tagging system

## Slide 9
A
1
2
3
4
D
E
F
B
1
2
3
4
C
1
2
3
4
Routing:
D->A->B->E
D->A->C->B-E
E->B->A->D
E->B->C->A->D
D->A->C->F
D->A->B->C->F
F->C->A->D
F->C->B->A->D
E->B->C->F
F->C->B->E
E->B->A->C->F
F->C->A->B->E
Assume we send packets with initial TTL=8
N = {
(D, 8), (A1, 7), (B1, 6), (E1, 5),
(D, 8), (A1, 7), (C1, 6), (B4, 5), (E1, 4),
(E, 8), (B2, 7), (A3, 6), (D1, 5),
(E, 8), (B2, 7), (C3, 6), (A4, 5), (D1, 4),
(D, 8), (A1, 7), (C1, 6), (F1, 5),
(D, 8), (A1, 7), (B1, 6), (C3, 5), (F1, 4),
(F, 8), (C4, 7), (A4, 6), (D1, 5),
(F, 8), (C4, 7), (B4, 6), (A3, 5), (D1, 4),
(E, 8), (B2, 7), (C3, 6), (F1, 5),
(F, 8), (C4, 7), (B4, 6), (E1, 5),
(E, 8), (B2, 7), (A3, 6), (C1, 5), (F1, 4),
(F, 8), (C4, 7), (A4, 6), (B1, 5), (E1, 4)
}
The grey ones are duplicated. We sort N by TTL:
N={
(D, 8), (E, 8), (F, 8), (A1, 7), (B2, 7), (C4, 7), (B1, 6), (C1, 6),
(A3, 6), (C3, 6), (A4, 6), (B4, 6), (E1, 5), (B4, 5), (D1, 5), (A4, 5),
(F1, 5), (C3, 5), (A3, 5), (C1, 5), (B1, 5), (E1, 4), (D1, 4), (F1, 4)
}
1
1
1

## Slide 10
N={
(D, 8), (E, 8), (F, 8), (A1, 7), (B2, 7), (C4, 7), (B1, 6), (C1, 6),
(A3, 6), (C3, 6), (A4, 6), (B4, 6), (E1, 5), (B4, 5), (D1, 5), (A4, 5),
(F1, 5), (C3, 5), (A3, 5), (C1, 5), (B1, 5), (E1, 4), (D1, 4), (F1, 4)
}
D,8
E,8
F,8
A1,7
B2,7
C4,7
A3,6
A4,6
B1,6
B4,6
C1,6
C3,6
A3,5
A4,5
D1,5
B1,5
B4,5
E1,5
C1,5
C3,5
F1,5
D1,4
E1,4
F1,4
Lossless Graph G

## Slide 11: Alg. 1
D
E
F
B2
A1
C4
A4
A3
B4
B1
C3
C1
D1
S2={
(D, 8), (E, 8), (F, 8), (A1, 7), (B2, 7), (C4, 7), (B1, 6), (C1, 6),
(A3, 6), (C3, 6), (A4, 6), (B4, 6), (B4, 5), (A4, 5), (B1, 5),
(D1, 5), (E1, 5), (F1, 5),
}
S1={
(C3, 5), (A3, 5), (C1, 5), (E1, 4), (D1, 4), (F1, 4)
}
Inter-Si edges:
(B1, 6)(C3, 5), (B4, 6)(C3, 5),
(B1, 6) (A3, 5), (B4, 6) (A3, 5),
(A3, 6)(C1, 5), (A4, 6)(C1, 5),
(A4, 5)(D1, 4), (B1, 5)(E1, 4), (B4, 5)(E1, 4),
E1
F1
A3
C3
C1
D1
E1
F1
A4
A3
B4
B1

## Slide 12: Alg. 2
Two lossless classes (class 2 and class 1), one lossy class (class 0)
24 ACL rules
  18 for class 2, 6 for class 1
PFC-priority map config on 4 ports (for inter-Si edges)