## Slide 1
Combating Deadlock in RDMA Data Center Networks

## Slide 2
Advantages of RDMA Data Center Networks
Ultra-low latency
High throughput
Very low CPU overhead

## Slide 3
RDMA is Not Robust by Itself
PFC is key for providing a lossless L2 network as PFC pause frames can always prevent packet loss in time under normal circumstance.
PFC is not for free because it can create deadlock
  Routing loop can cause PFC deadlock.
  Cyclic routing dependency can cause PFC deadlock.
  Device bugs can cause PFC deadlock.

## Slide 4
H2: 10.1.1.1
H1: 10.0.0.1
10.0.0.0/16 -> Aggr 1,2
10.1.1.0/24 -> ToR 4
Default -> Core 1,2
10.1.0.0/16 -> Aggr 3,4
10.1.0.0/24 -> ToR 3
Aggr 3
ToR 3
Aggr 4
ToR 4
Aggr 1
Aggr 2
ToR 2
ToR 1
Core 1
Core 2
Loop-Induced Deadlock Case in Clos

## Slide 5
H3: 10.1.0.1
H2: 10.0.1.1
H4: 10.1.1.1
H1: 10.0.0.1
Aggr 3
ToR 3
Aggr 4
ToR 4
Aggr 1
Aggr 2
ToR 2
ToR 1
Core 1
Core 2
Flow 2
Flow 1
Flow 3
Cyclic Routing Induced Deadlock Case in Clos

## Slide 6
Core1
Aggr2
Aggr3
Core2
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
Flow 3
Cyclic Routing Induced Deadlock Case in Clos

## Slide 7
Device Bug Induced Deadlock Case
A deadlock caused by packet flooding bug of Arista switch.

## Slide 8
Analysis of Loop-Induced Deadlock

## Slide 9
Loop-Induced Deadlock - Routing loop Deadlock
H2: 172.16.4.5
H1: 172.16.3.6
172.16.4.0/31 -> T2
L1
L2
T2
T1
172.16.4.5/32 -> L2
Inject Lossless traffic into a 2-hop routing loop:
Routing loop is just a necessary condition because TTL expiration of packets will prevent packets from building up in the loop.
Injection rate | Deadlock
4Gbps | No
5Gbps | No
6Gbps | Yes
TTL =16, Link capacity = 40Gbps:

## Slide 10
Loop-Induced Deadlock – Impact of TTL Expiration
r
B - rd
B
Two equations under stable state:
  input rate is equal to output rate: ;
  TTL conservation: .
r | Inject rate of new packets.
B | Link bandwidth.
rd | Packets drain rate caused by TTL expiration.
TTL | TTL value.
n | Hop number of the routing loop.
Basic Model
TTL drain rate
TTL generating rate
Solution of Stable State:
Sufficient condition for packets to build up in a loop system:
…
q1
q2
qn

## Slide 11
Verification of Basic Model – Exp A
Observation: basic model provides a good lower-bound rate above which queue will build up.
We inject lossy UDP traffic into a 2-hop loop, and measure the minimum input rate at which queue will build up:

## Slide 12
Loop-Induced Deadlock - Consider PFC
Consider PFC
tPFC
r
B - rd
B
…
q1
q2
qn
Question: what is the sufficient condition for packets to build up when PFC is considered?

## Slide 13
Loop-Induced Deadlock – Queueing Delay
r = 1Gbps
B=40Gbps
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
#2 | 2 | 0 | 13
#3 | 4 | 0 | 11
#4 | 6 | 0 | 9
#5 | 8 | 0 | 7
#6 | 10 | 0 | 5
#7 | 12 | 0 | 3
#8 | 14 | 0 | 1
Round | Time unit | Queueing delay | Remaining TTL
#1 | 0 | 0 | 15
#2 | 2 | 1 | 13
#3 | 5 | 4 | 11
#4 | 11 | 10 | 9
#5 | 23 | 22 | 7
#6 | 47 | 46 | 5
#7 | 95 | 94 | 3
#8 | 191 | 190 | 1
r = 40Gbps
B=40Gbps
Expiration time of the 1st pkt
Expiration time of the 1st pkt
TTL=16
TTL=16
Case 1: r = 1Gbps < , packets will not build up.
Case 2: r = 40Gbps > , packets will build up.
      Observation: Once packets are queued in the loop, rd will be significantly reduced by queueing delay in the loop.

## Slide 14
Loop-Induced Deadlock - Consider PFC
Consider PFC
tPFC
r
B - rd
B
…
q1
q2
qn
Question: what is the sufficient condition for queues to build up when PFC is considered?
Answer: 1) As PFC ensures per ingress fair sharing, r can be at most reduced by half due to PFC pause. 2) rd is reduced by at least one order due to queueing delay in the loop before PFC threshold is even reached. So the sufficient condition still holds when PFC is considered.
Sufficient condition for loop-induced deadlock:

## Slide 15
Observation: our basic model does not consider the impact of PFC pause, but it still provides a good lower-bound input rate above which PFC deadlock will occur
Verification of Basic Model – Exp B
We inject lossless UDP traffic into a 2-hop loop, and measure the minimum input rate at which PFC deadlock will occur:

## Slide 16
Lower-bound Deadlock Time: n*tPFC/
Upper-bound Deadlock Time: n*tPFC/(-)
Observation: when the sufficient condition is met, we have >= r/2, rd << and <r. So lower-bound estimation is a tight estimation.
Loop-Induced Deadlock – Deadlock Time

## Slide 17
Observation: Lower-bound estimation is a tight bound.
Verification of Estimation of Deadlock Time– Exp C
We inject lossless UDP traffic into a 2-hop loop, and measure the deadlock time:
(a) Setting: TTL = 64, α = 1/32 (no PFC deadlock when r < 1.3Gbps).
(b) Setting: TTL = 64, α = 1/64 (no PFC deadlock when r < 1.3Gbps).

## Slide 18
Analysis of Non-loop Routing-Induced Deadlock

## Slide 19
Non-Loop Deadlock –
Cyclic Routing Dependency Deadlock
r1 = B
In this case, cyclic routing dependency is met but no deadlock.
Cyclic routing dependency is just a necessary condition as it is not guaranteed that all the links will be paused.
S2
S1
S3
S4
rx
tx
rx
rx
rx
tx
tx-1
tx
tx-2
Flow 2
Flow 1
r2 = B
L1
L2
L3
L4

## Slide 20
rate limit=1/4
rate limit=1/4
S2
S1
S3
S4
RX 1
TX
RX 2
RX 3
TX-1
TX-1
TX
TX-2
Flow 2
Flow 1
r1 = B
r2 = B
TX-2
RX 4
Non-Loop Deadlock –
Simultaneous Pause Deadlock
In this case, all the links in the cycle are paused at the same time but no deadlock.
Simultaneous Pause is just a necessary condition as it is not guaranteed that all the pauses will not be resumed.
Flow 4
Flow 3

## Slide 21
Deadlock Prediction is not a trivial thing.
Two algorithms for deadlock prediction:
    Non-lineal Fluid Model with Differential Equations (currently don’t know how to solve the equations)
    Iterative Algorithm based on Statistical Model (currently don’t know how to prove the correctness)
Using simulations to demonstrate that both algorithms can correctly predict whether deadlock will happen for the 6 deadlock scenarios.
Non-Loop Deadlock – Deadlock Prediction

## Slide 22
Solution for Preventing Deadlock in Clos Network
H1: 10.0.0.1
Aggr 3
ToR 3
Aggr 4
ToR 4
Aggr 1
Aggr 2
ToR 2
ToR 1
Core 1
Core 2
H2: 10.1.1.1
Priority = 1
Priority = 1
Priority = 2
Priority = 2
Key Idea: we increase the packet priority of a flow each time the flow changes its direction from DOWN to UP. We drop the packet when no higher priority is available.

## Slide 23
Solution for Preventing Deadlock in Clos Network
Notation: Let li be the i-th link in the deadlock cycle. pi be the highest priority of the packets traversing link li. pmax be the highest priority in the deadlock cycle. Fk be the set of flows traversing lk with the highest priority. Slow be the switch of the lowest network level in the cycle.
Proof: We assume deadlock still happens under this solution. We consider whether the packets of the highest priority in the cycle will be paused permanently.
The strategy here is to set the priority of one flow at a link to be once this flow will not be permanently paused at this link.
Highest Priority of ln = pn
l1
l2
l3
…
ln
Highest Priority of l3 = p3
Highest Priority of l2 = p2
Highest Priority of l1 = p1

## Slide 24
Solution for Preventing Deadlock in Clos Network
Case 1: p1= p2 =… =pn is not satisfied.
(1) In this case, we can always find one link lk where pk = pmax and pk > p(k+1).
(2) ∀f, f will not traverse lk+1. Otherwise, pk > p(k+1) will be violated.
(3) Packets with priority pk will not be permanently paused at link lk.
(4) We set all the flows ({f| f }) traversing lk with priority .
(5) Repeating (1) - (4), we can set the highest priority pk to be at all links.
pk > p(k+1)
l1
l2
lk
…
…
lk+1
Notation | Description
li | the i-th link in the deadlock cycle
pmax | the highest priority in the deadlock cycle
pi | the highest priority of the packets traversing link li
Fk | the set of flows traversing lk with the highest priority pi

## Slide 25
Solution for Preventing Deadlock in Clos Network
l1
l2
lk
…
Case 2: p1= p2 =… =pn is satisfied.
(1) In this case, we can always find link lk and link lk+1 connection with Slow .
(2) ∀f, f will not traverse lk+1. Otherwise, pk+1 = pk will be violated.
(3) Packets with priority pk will not be permanently paused at link lk.
(4) We set all the flows ({f| f }) traversing lk with priority .
(5) Case 2 comes back to Case 1.
…
lk+1
fk
Slow
Notation | Description
li | the i-th link in the deadlock cycle
Slow | the switch of the lowest network level in the cycle.
pi | the highest priority of the packets traversing link li
Fk | the set of flows traversing lk with the highest priority pi

## Slide 26
Solution for Preventing Deadlock in Clos Network
l1
l2
lk
…
At any round, either it satisfies case 1 or case 2, we can always change the highest priority to at all the links. Following this procedure, we can prove that no packets can be permanently paused in the cycle.
…
lk+1